## Slide 1
Flood Management & Water Quality Measurement using 5G IoT
Sardar Vallabhbhai National Institute of Technology , Surat - 395007
Presentated by,
Kalpesh Parmar (U21EC103)
Aayush Parikh (U21EC126)
Mihir Solanki (U21EC161)
A
Project Presnetaion
Entitled
Guided by,
Dr. (Ms.) Shilpi Gupta
(Associate Professor, DoECE)
Co-Guided by,
Dr. Raghavendra Pal
(Assistant Professor, DoECE)

## Slide 2
Flood Management and Water Quality Measurement using 5G-IoT
Objective: To address flood risks and water quality concerns by continuously monitoring key environmental metrics.
Technologies Used: Utilizes IoT sensors and 5G technology for fast, real-time data transmission and monitoring.
Key Metrics: Monitors water levels, pH, turbidity, TDS, and rainfall intensity to assess flood risk and water quality.
Target Outcomes: Aims to improve disaster preparedness and efficient resource management through real-time monitoring.

## Slide 3
Working and Process Flow
Data Collection: Sensors measure water levels, rainfall, pH, turbidity, and TDS in real time.
Data Transmission: Collected data is sent to the Bharat Pi module using 5G for fast and reliable connectivity.
Edge Computing: Local processing of data minimizes latency and enables immediate analysis
Cloud Integration: Processed data is uploaded to the cloud for storage and visualization.
Decision Support System: Insights from the processed data assist in effective planning and response strategies during floods or water quality issues.

## Slide 4
System Components
  Bharat Pi 4G LTE Module for connectivity:Provides reliable internet connectivity for remote data transmission via 4G LTE.
  Ultrasonic Sensor for water level detection: Measures water levels in real-time to predict flood risks.
  Raindrop Sensor for precipitation monitoring: Detects rainfall intensity to aid in flood prediction and monitoring.
  pH and Turbidity and TDS Sensors for water quality analysis: Measures the pH and turbidity levels of water to assess its cleanliness and safety.
  Cloud platform for data storage and visualization: Stores and visualizes the data for analysis and decision-making.

## Slide 5
Achievements and Future Scope
Real-time monitoring capabilities for floods and water quality: Provides instant data on water levels and quality to aid decision-making.
Scalable and modular architecture: The system can be expanded to include more sensors and regions as needed.
Renewable energy integration for remote setups: Future systems may use solar or wind power to operate sensors in off-grid locations.
Potential for integration with smart city infrastructure: The system can be integrated with smart city networks for enhanced disaster management and resource monitoring.
Support for Sustainable Development Goals (SDGs): Contributes to SDGs by promoting sustainable water use and environmental protection

## Slide 6
Bharat Pi: An Evolution in Microcontrollers
Bharat Pi
Microcontroller: 32-bit Dual Core, 160 MHz (10 times faster than Arduino Uno)
RAM: 512 KB (256x more memory space).
Flash Memory: 16 MB (can handle larger codebases, such as 1000+ lines of code).
Network: Built-in Wi-Fi and Bluetooth for internet connectivity.
GPIO Pins: 36 General Purpose I/Os (can connect 2.5x more sensors).
Bus Interfaces: SPI, I2C, 2xUART, I2S, CAN (more UART and CAN interface options).
ADC Channels: 18 Analog-to-Digital Converters (can connect 3x more analog sensors).
Data Storage: Supports an SD Card up to 128 GB (ideal for AI/ML edge data mining).
Arduino Uno
Microcontroller: 8-bit Single Core, 16 MHz.
RAM: 2 KB.
Flash Memory: 32 KB.
Network: No built-in connectivity (requires external modules for Wi-Fi or Bluetooth).
GPIO Pins: 14 General Purpose I/Os.
Bus Interfaces: SPI, I2C, UART.
ADC Channels: 6 Analog-to-Digital Converters.
Data Storage: No SD card support.

## Slide 7
Flood Management
Rain Sensor
3Detects rainfall effectively using changes in conductivity due to water.
Water Flow Sensor (YF-S201)
Measures water flow accurately for discharge monitoring using rotational pulse-based measurement.
Ultrasonic Sensor (HC-SR04)
Measures water level accurately and cost-effectively using ultrasonic wave reflection.

## Slide 8
WaterQuality Measurement
pH Sensor
Monitors water acidity or alkalinity through hydrogen ion concentration, a crucial parameter for water quality.
Turbidity Sensor
Measures water cloudiness effectively for sedimentation monitoring by detecting optical suspended particles.
Total Dissolved Solid
The TDS Sensor measures total dissolved solids in water using electrical conductivity, providing an indication of water purity.

## Slide 9
Data Analysis
We use ThingSpeak and a custom-built website to collect, visualize, and analyze real-time sensor data. This platform allows us to monitor water parameters through interactive graphs for better flood management and water quality assessment.
• Water Level (Ultrasonic Sensor HC-SR04):– We can collect data in real-time to monitor the water level in reservoirs, rivers, or lakes.– Example: Sudden spikes in water levels could indicate the risk of flooding.– Measurement units: centimeters (cm) or meters (m) now made same for water flow sensor

## Slide 10
Data Analysis
Water Flow (YF-S201 Sensor): Real-time data monitors water flow in pipelines, rivers, or irrigation systems, with sudden increases indicating pipe bursts or flooding, and reduced flow signaling blockages or drought conditions. Measurement units: L/min or m³/h.
Real-time data from the water flow sensor is used to plot the speed of water passing through the sensor over time.
The total volume of water is calculated by integrating the flow rate data over time and displayed on a graph.

## Slide 11
01
Issues Faced During Component Procurement and Integration
Constraints in Data Accuracy & Connectivity
Enhancing Sensor Coverage and Accuracy
Scaling the System for Large Geographical Areas
02
03
04
Challenges
&
Limitations

## Slide 12
Issues Faced During Component Procurement and Integration
  Availability of Components
  Cost Constraints
  Component Compatibility
  Power Supply Integration
01

## Slide 13
Constraints in Data Accuracy & Connectivity
  Sensor Accuracy
  Environmental Factors
  Data Latency
02

## Slide 14
Enhancing Sensor Coverage and Accuracy
  Expanded Sensor Deployment
  Improved Sensor Technology
  Integration of Advanced Communication Protocols
03

## Slide 15
Scaling the System for Large Geographical Areas
  Distributed Architecture
  Interconnected Network of Systems
  Integration with Smart City Infrastructure
04

## Slide 16
Conclusion
  Advanced Monitoring Capabilities
  Scalability and Flexibility
  Energy Efficiency and Sustainability
  Proactive Disaster Management
  Support for Sustainable Development Goals (SDGs)
  Improved Water Quality Management
*
*
*
*

## Slide 17
Thank you

## Slide 18
Questions
&
Answers